PAKISTAN REVENUE AUTOMATION (PVT.) LIMITED

Invitation for Bids

Ref. Admin/P&D-Cabling/PRAL/HQs/2009		     		       	         January 17, 2009

Subject:	TENDER NO. ADMN(G-01)/2009 DATED 17/01/2009 FOR SUPPLY AND INSTALLATION OF DATA CABLING, ELECTRICAL / POWER CABLING AND TELEPHONE CABLING..

1.	Pakistan Revenue Automation (Pvt.) Ltd. (hereinafter called PRAL/Purchaser) invites sealed bids for supply and installation (on most urgent basis) of Data and Electrical / Power cabling and Telephone Cabling at House # 14, Hill Road, F-6/3, Islamabad as per detail / specifications described in the BOQ “Annexure- A”.

2.	All Government Taxes shall be deducted as per law.

3.	PRAL reserves the right to increase or decrease the quantity of the items given in the BOQ, accept or reject any bid to be received against this tender inquiry, annul the bidding process and reject all bids at any time prior to award of Contract (s) without thereby incurring any liability to the affected Bidder or Bidders or any obligation to inform the affected Bidder or of the grounds for PRAL’s action.

4.	DELIVERY SCHEDULE

The supply and installation of the cabling works given in the BOQ is required on most urgent basis. So the lowest technical compliant bidder may be in a position to supply and install the order material as immediately as possible after award of the contract.

5.	PENALTY:

For failure to comply with the delivery schedule of Purchase Order (s), to be issued against this tender documents penalty will be imposed on defaulting Supplier as under:

5.1	1% of the cost of entire purchase order or of such item as remain un-supplied/un-completed for every day up to maximum of 5% for 10 days exceeding the delivery period.

5.2	If the item is not supplied even after payment of penalty for 10 consecutive days PRAL reserves the right to cancel the purchase order and to purchase required equipment from elsewhere at risk and cost of the defaulting Supplier.

6.	Quoted prices must be inclusive of all taxes (Income Tax and Sales Tax), indicating unit price and total bid price.

7.	Price must be quoted including all charges like handling, loading, transportation, unloading of the equipment at Islamabad. Quoted prices must also be inclusive of cost for the free maintenance of equipment on installation site during warranty period.

8.	Bidding Form Annexure “B” must also be duly filled in, stamped and signed by authorized representative of the bidder.

9.	Quoted price shall be valid for 120 days from the opening date of the bids. However, any subsequent change in taxes and duties as notified by Central Board of Revenue will be given due consideration.

10.	PAYMENT:

100% payment of the total value of the bill/purchase order will be released subject to Completion of the delivery of the equipment in accordance with the specifications mentioned in this tender document or Purchase Order to be issued against this tender and submission of bank guarantee as described under clause “18” of the tender documents.

11.	SEALING AND MARKING OF BIDS.

11.1	The bids shall be submitted in sealed envelope marked as under:

MANAGER (ADMINISTRATION)

PAKISTAN REVENUE AUTOMATION (Pvt.) LIMITED

HOUSE # 15, STREET # 19, F-6/2, ISLAMABAD.

11.2	The envelopes shall also bear the word “CONFIDENTIAL” and following identifications:-

BID NO. ADMN(G-01)/2009

For Supply And Installation Of Data And Electrical / Power Cabling and Telephone Cable.

12.	DEADLINE FOR SUBMISSION OF BIDS:

All bids must be delivered in the Office of undersigned on or before the prescribed deadline of 1100 hours on 04/02/2009.

13.	OPENING OF BIDS:

The Purchaser will open the bids in the presence of bidder representatives who choose to attend at 1130 hours on 04/02/2009 at the below mentioned address.

14.	WARRANTY

14.1	The Supplier shall warrant that all equipment supplied against the Purchase Order (s) shall have no defect arising from design, materials or workmanship or from any act or omission of the Supplier, that may develop under normal use of the supplied items under the conditions prevailing at final destination.

14.2	Period of Warranty and maintenance with labour and material cost shall be SIX Months.

During warranty period the supplier will be responsible to repair/replace the faulty equipment on installation place free of cost within 24 hours after occurrence of fault

15.	All bids should include:

15.1	Company’s profile, list of clients with their telephone number and address;

15.2	Copies of Income Tax and Sales Tax registration certificates;

16.	PRAL reserves the right to accept or reject any bid and to annul the bidding process and reject all bids at any time prior to award of Contract (s) without thereby incurring any liability to the affected Bidder or Bidders or any obligation to inform the affected Bidder or of the grounds for PRAL’s action.

17.	If you have any doubt as to the meaning of any portion of the technical specifications, you may seek clarification of the same from Syed Mubashir Hussain Shah, Administrative Officer, 5th floor, Evacuee Trust Complex, Islamabad. Cell # 0323-5159233.

## 18.	BANK GUARANTEE

After completion and acceptance of the Project by PRAL, the bidder will have to provide the Bank Guarantee, being 10% of the total value of the bill/Contract, issued by renowned Schedule Bank, for the warranty/maintenance period to be offered. In case the supplier failed to provide the Bank Guarantee 10% of the total bill value shall be retained by PRAL for the successful completion of warranty period. The Bank Guarantee shall be released after successful completion of warranty period. In case the supplier failed to complete the warranty period successfully then the retained value/bank guarantee shall be forfeited in favour of PRAL.

.

# (SOHAIL AKHTAR)

Manager (Administration.)

House # 15, Street # 19, F-6/2, Islamabad.

Phone:	9208687

ANNEXURE-A

SCHEDULE OF REQUIREMENT

TENDER # ADMN(G-01)/2009 DATED 17/01/2009

1.	LAN Cabling Specifications                                                                                   (150 Nodes complete with I/O faceplates, drop cables, Patch Panels and accessories)

- Cat 6 Cabling required on turnkey basis.

- Cable should be of type Corning/Ortronics/Nordex/AMP.

- Providing and installing UTP Cat-6 cable with RJ45 I/O complete with back box hardware.

- Termination on 24 port Cat-6 patch panel (patch panel included) proper tags with Tie and dressing between switch and patch panel.

- All product range to be of same manufacturer with UL, cUl, NCSA certified cable.

- Performance must meet class E TIA / EIA channel specifications for category 6 cable must support giga byte Ethernet.

- Color dressing is required between patch panel and switch for identification.

- Cabling cost should be given on per Network Node Basis (Complete setup including Patch Panels, IO’s, Patch cords of 3 meter and 1 meter, Ducts etc). Each rack will have a 24 port Patch Panel.

- All cabling has to be done in PVC channels/pipes.

2.	POWER CABLING SPECIFICATIONS

(300 Power Points complete with installation of Power DB's breaker and all accessories)

Supply, Installation, Termination & Testing of the Electrical Wiring Setup on Turnkey Basis

- Installation of Independent Power DB from source for Power Setup which includes change over for future integration with genset

- Cable to be used in main hall which includes all offices and cubicles should be three core PVC coated 7/29, 99.99 % pure copper Pakistan or Pioneer cable

- Circuit breaker which should be used in power DB should be ABB or MG Brand only (vendors may use different breakers according to their power design)

- Original Clipsal Three Pin Flat/Round Sockets

- Tagging  for identification and management is required in power DB

- Separate Earth pit IS Required with Ratings less than 1 Volt

Note: A Detailed Survey is required for Electrical Setup

3.	TELEPHONE INTERCOM CABLING (50 Points)

Supply, Installation, Termination & Testing of the Telephone Intercom cabling on Turnkey Basis

- Installation of Independent management DB(box) for management

- Each point is properly tagged for easy identification and troubleshooting purpose

- Numbered tagging of each point

Note:

Vendors are requested to give their bids after site survey and inspection on per Node for LAN and per power point for power cabling. For supply and installation of telephone cable the vendor must also survey the site and thereafter submit their bids

ANNEXURE-"B"

BIDDING FORM

##### Dated 17/01/2009						    Tender No.ADMN(G-01)/2009

Pakistan Revenue Automation (Pvt.) Limited, Islamabad.

Gentlemen,

1.	Having examined the conditions to Tender and Specifications of Tender No.ADMN(G-01)/2009 dated 17/01/2009 the receipt of which is hereby acknowledged we, the undersigned, offer to install, supply and deliver in conformity with specifications mentioned in Annexure “A” and conditions of Tender for the sum of Rs._________________________ (Rupees ______________________________ ) or such other sums as may be ascertained in accordance with the said Conditions.

2.	If our Bid is accepted we shall deliver the equipment mentioned in the tender documents within ______ days from the date of receipt of your firm Purchase Order.

3.	We agree to abide by the terms and conditions of the Tender for the period of _______ from the date fixed for receiving the same and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

4.	Until a formal Purchase order(s) is placed, this Bid, together with your written acceptance thereof, shall constitute a binding contract between us.

5.	We understand that you are not bound to accept the lowest or any proposal you may receive or to inform us of the rejection of our bid or to give any reasons therefor.

Dated this ______________________ day of ______________________________ 2009_______________.

Signature _______________________ in the capacity of ______________________________ duly authorized to sign Tender for and on behalf of

_____________________________________________________________________________________

(NAME OF FIRM IN BLOCK CAPITALS)

Complete address:________________________________________________________________________

Fax No.____________________________ Telephone No.______________________________________

______________________

( SIGNATURE )

Witness:-

1.	_______________________

2.	_______________________