SHORT TENDER NOTICE NO.P-04/2011

Sealed bids are invited from the firms having registration with the Sales Tax and Income Tax Departments for urgent supply and installation of Layer 3 and Layer 2 Switches at FBR House, Islamabad. Detail Tender Documents may be obtained from the office of undersigned (during working hours) or download from www.ppra.org.pk or www.pral.com.pk from 18/03/2011 to 05/04/2011. Last date for submission of the bids is 05/04/2011 on or before 1200 hours. Bids shall be opened on the same day at 1230 hours.

Syed Waqar Gilani

Director (TARP / OMSD)

House # 14,  Hill Road, F-6/3, Islamabad.

Supply, Installation& Configuration of LAYER 3 AND LAYER 2 SWITCHES FOR FBR HOUSE ISLAMABAD

Pakistan Revenue Automation (Pvt.) Ltd.

TENDER NO.P-04/2011

DATED __18-03-2011________

Bid Submission on 05-04-2011________

TENDER DOCUMENT

Pakistan Revenue Automation Pvt. Limited

# Ref: Proc/Layer Switches/FBR/2011							Islamabad, March 18, 2010

Subject:	TENDER NO.P-04/2011 FOR THE PROCUREMENT OF LAYER 3 AND LAYER 2 SWITCHES FOR FBR HOUSE ISLAMABAD

1.	Pakistan Revenue Automation Pvt. Limited (hereinafter called PRAL/Purchaser) invites sealed bids for the for the supply & installation of Layer 3 and Layer 2 switches for FBR House, Islamabad as per detail given in Schedule of Requirement at  Annexure-“A”.

2.	If you have doubt as to the meaning of any portion of the specifications or other terms and conditions you may seek clarification of the same in writing from Mr. Ali Hameed, Director (Networks & Infrastructure) PRAL., Ph # 051-9204952 Cell # 0321-5591498 / Malik Nasir Abbas, Manager (Infrastructure) PRAL, Cell # 0321-5371151.

3.	PRAL reserves the right to increase or decrease the quantity, accept or reject any bid to be received against this tender inquiry, annul the bidding process and reject all bids at any time prior to award of Contract (s) without thereby incurring any liability to the affected Bidder or Bidders or any obligation to inform the affected Bidder or of the grounds for PRAL’s action.

4.	Income Tax / Withholding Tax will be deducted in accordance with the law. Kindly note that the Sales Tax shall also be deducted in accordance with the law.

5.	DELIVERY SCHEDULE

The delivery / installation/testing/commissioning/configuration etc of the equipment mentioned in Schedule of Requriement Annexure “A” is required within 6-8 weeks (in Islamabad) after award of the contract(s) to be issued against this tender inquiry. So the lowest technical complaint bidder may be in a position to complete delivery, installation, testing commissioning and configuration within the given time frame.

6.	PENALTY:

For failure to comply with the delivery schedule of Purchase Order (s), to be issued against this tender documents penalty will be imposed on defaulting Supplier as under:

6.1	1% of the cost of entire purchase order or of such item as remain un-supplied/un-completed for every day up to maximum of 5% for 10 days exceeding the delivery period.

6.2	If the item is not supplied even after payment of penalty for 10 consecutive days PRAL reserves the right to cancel the purchase order and to purchase required equipment from elsewhere at risk and cost of the defaulting Supplier.

7.	Quoted prices must be inclusive of all taxes (Income Tax and Sales Tax), indicating unit price and total bid price.

8.	Price must be quoted including all charges like handling, loading, transportation, unloading of the equipment at Islamabad. Quoted prices must also be inclusive of cost for the free maintenance of equipment on installation site during warranty period.

9.	Bidding Form Annexure “B” must also be duly filled in, stamped and signed by authorized representative of the bidder.

10.	Quoted price shall be valid for six (6) months from the opening date of the bids. However, any subsequent change in taxes and duties as notified by Federal Board of Revenue will be given due consideration.

11.	EARNEST MONEY:

The Bidder shall furnish as part of his bid, a Call Deposit/Pay Order equivalent to 2% of the total bid value as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.”. Any bid not accompanied by Earnest Money shall be rejected without any right of appeal. In case of cancellation of Purchase Order as default of the Supplier the earnest money shall be forfeited in favour of PRAL. Bank Guarantee as earnest money shall not be acceptable.

12.	PAYMENT:

100% payment of the total value of the bill/purchase order will be released subject to:

12.1.	Completion of the delivery, installation, testing,  commissioning, configuration etc of the equipment in accordance with the specifications mentioned in this tender document or Purchase Order(s) to be issued against this tender;

12.2.	Submission of Bank Guarantee (to be issued by any renowned schedule bank) being 10% of the total bill value for the warranty period. The Bank Guarantee shall be released after successful completion of warranty period. Failing to provide bank guarantee 10% of the bill shall be retained till to the successful expiry of the warranty period;

13.	SEALING AND MARKING OF BIDS.

13.1	The bids shall be submitted in sealed envelope marked as under:

Director (TARP/OMSD)

House # 14, Hil Road, Sector F-6/3, Islamabad

13.2	The envelopes shall also bear the word “CONFIDENTIAL” and following identifications:-

BID NO. P-04/2011

For purchase of Layer 2 & Layer 3 Switches

14.	DEADLINE FOR SUBMISSION OF BIDS:

All bids must be delivered in the Office of undersigned on or before the prescribed deadline of 1200 hours on 05/04/2011.

15.	OPENING OF BIDS:

The Purchaser will open the bids in the presence of bidder representatives who choose to attend at 1230 hours on 05/04/2011 at the below mentioned address.

16.	WARRANTY

16.1	The Supplier shall warrant that all equipment supplied against the Purchase Order (s) shall have no defect arising from design, materials or workmanship or from any act or omission of the Supplier, that may develop under normal use of the supplied items under the conditions prevailing at final destination.

16.2	Period of Warranty and maintenance with labour and material cost shall be “three (3) years comprehensive”.

During warranty period the supplier will be responsible to repair/replace the faulty equipment on installation place free of cost within 24 hours after occurrence of fault. During warranty period due to any reason, if the Supplier failed to rectify the problem, PRAL shall repair the equipment or replace the defective parts thereof and forfeit the Bank Guarantee/retained values.

17.	All bids should include:

17.1	Company’s profile, list of clients with their telephone number and address;

17.2	Copies of Income Tax and Sales Tax registration certificates;

17.3	A call deposit being 2% of the total bid value as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.; and

17.4	Brochures and other technical material of the quoted equipment.

17.5	Certificate from the principal that the vendor is Sole Distributor / Authorized Dealer / Authorized Re-Seller etc.

17.6	Assurance from the principal that if the local vendor fails to provide the required support, Principal shall provide the required support.

17.7.	Assurance in writing that bidder will maintain the equipment fully functional with a down time of less than 24 hours.

17.8.	Affidavit (on legal paper) that the vendor is neither blacklisted nor in litigation with any of its clients.

18.	PRAL reserves the right to increase or decrease the quantity of the equipment mentioned in the Schedule or Requirement

# (SYED WAQAR GILANI)

Director (TARP/OMSD)

House # 14, Hil Road, Sector F-6/3, Islamabad

ANNEXURE-A

SCHEDULE OF REQUIREMENT

TENDER # P-04/2011, DATED 18/03/2011

Technical Specifications of Layer 3 for FBR House

### 800+ Gbps Backplane

### Switching Fabric 380+ Gbps with Required Installed Modules

### Packet Forwarding 280+ Mppswith required Installed Modules

### Modular Chassis

### 2 x CP’s or Control modules with for Redundancy / Load Sharing

### 1 x 48 10/100/1000 GE Slot

### 2 x 24 SFP for Multimode with 34 x SX and 14 x TX Modules

### Redundant N+1 Power Supply

### Advanced Routing License

### Advanced Security License

### Advanced L2/L3/L4 ACL

### 100K MAC Address Support, STP 802.1D, ARP, RSTP, MSTP support, flow control

### Port mirroring Support, Trunking Support / Traffic Redirection

### NAT, PAT, Advanced IP Access Control List License

### 802.1Q , 4000+ VLANs, Port Based VLAN, Protocol Based VLAN,

### IP-MAC-Port Binding

### QoS , 802.1p, & Bandwidth Management , Rate Limiting for End-Users , Bandwidth Control Down to 512 Kbits for Ingress and Egress traffic and Traffic Classification (with License if Required )

### Access control List 25k rules per Chassis based on Port, MAC, VLAN, 802.1p, protocol type, TOS, IPv4/v6 Address, TCP/UDP ports and DSCP

### 802.1D/w/s Spanning Tree, 802.3ad

### Link Aggregation/Backup Redundancy

### RIP v1 /v2 , OSPF v2 / v3 , BGP4 , MPLS, Policy Based Routing , IPv6 Tunneling and VRRP Support

### Multicast, IGMP support v1,v2,v3

### Telnet/CLI/SNMP v1, v2c, v3 Management

### RMON Monitoring

### System/Alert Information, Interface Management

### DHCP, DHCP server Relay support, TFTP, FTP, HTTP

### 802.1v Protocol VLAN, Super VLAN, Private VLAN, Double VLAN

### L3 Protocol-Based Policies

### 802.1x , Radius, Accounting support

### MIB support

### Enterprise Management Software

### 3 Years Technical Support License Directly from Principle on account of FBR for 24x7 support ,troubleshooting and Upgrades.

### All Allied software’s and Cables Required

### Technical Specifications of Layer 2 switch for FBR House

- 1x 24 10/100/1000 ports + 2 SFP for Multimode

- Switching Capacity : 68+ Gpps

- Forwarding Rate: 50+ Mpps

- IEEE 802.3 compliance

- IEEE 802.3u compliance

- IEEE 802.3ab compliance

- Support Half/Full-Duplex operations

- Auto-negotiation

- Auto MDI/MDIX

- IEEE 802.3x Flow Control support for Full-Duplex mode

- 8K MAC Address Table

- Support 256 static MAC

- STP, 802.1D,802.1s,802.1W

- 802.3ad Link Aggregation

- Max 256 static VLAN groups , Max 256 dynamic VLAN groups

- Configurable vid from 1~4094

- VLAN Trunking,

- Port Mirroring , one to one , one to many

- ACL Policy Support, VLAN, MAC, ether type etc

- Bandwidth control

- RADIUS , TACACS, 802.1p Support

- SNMP, Telnet, CLI, HTTP, FTP, TFTP, DHCP, SSHv1, SSHv2 etc

- Allied Cables and Accessories

- 3 Years Technical Support License Directly from Principle on account of FBR for 24x7 support , troubleshooting and Upgrades.

Bill of Quantity

| S. No | DESCRIPTION | Quantity |
| --- | --- | --- |
|  | Layer 3 Switch | 1 |
|  | Layer 2 Switch | 18 |

ANNEXURE-B

BIDDING FORM

##### Date:_________								           Tender No.P-04/2011

Pakistan Revenue Automation (Pvt.) Limited, Islamabad.

Gentlemen,

1.	Having examined the conditions to Tender and Specifications of Tender No.P-04/2011 dated 18/03/2011, the receipt of which is hereby acknowledged we, the undersigned, offer to install, supply and deliver in conformity with terms and conditions and specifications mentioned in Tender for the sum of Rs._________________________ (Rupees _____________________________) or such other sums as may be ascertained in accordance with the said Conditions.

2.	If our Bid is accepted we shall deliver the equipment specified in the Tender Documents within ___________ from the date of receipt of your firm Purchase Order.

3.	We agree to abide by the terms and conditions of the Tender for the period of _______ from the date fixed for receiving the same and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

4.	Until a formal Purchase order(s) is placed, this Bid, together with your written acceptance thereof, shall constitute a binding contract between us.

5.	We understand that you are not bound to accept the lowest or any proposal you may receive or to inform us of the rejection of our bid or to give any reasons therefore.

Dated this ______________________ day of ______________________________ 2011___________________

Signature _______________________ in the capacity of ______________________________ duly authorized to sign Tender for and on behalf of

___________________________________________________________________________________________

(NAME OF FIRM IN BLOCK CAPITALS)

Complete address:____________________________________________________________________________

Fax No.____________________________ Telephone No.________________________________________

______________________

( SIGNATURE )

Witness:-

1.	_______________________

2.	_______________________