SHORT TENDER NOTICE NO.ADMIN(G-08)/2012

Sealed bids are invited from the firms registered with the sales tax and income tax department for IMMEDIATE supply and installation of 60KVA generator and 30KVA UPS (one each). Tender Documents containing terms and conditions, technical details   and quantity of the material may be obtained from the office of undersigned (during office hours) or may download from www.ppra.org.pk or www.pral.com.pk from 25/09/2012 to 10/10/2012. Last date for submission of bids is 10/10/2012 on or before 1100 hours. The bids shall be opened on 10/10/2012 at 1130 hours in the presence of the bidder’s representatives.

Manager (Procurement)

House # 2-A, Embassy Road, Sector G-6/4, Islamabad.

Ph: 051-9208687

TENDER DOCUMENT

PAKISTAN REVENUE AUTOMATION (PVT.) LIMITED

Ref. Proc-Generator/UPS/PRAL/2012       		    		       	         	 	  September 25, 2012

Subject:	TENDER NO. ADMIN(G-08)/2012 DATED 25/09/2012 FOR THE SUPPLY & INSTALLATION OF 60 KVA GENERATOR AND 30 KVA UPS AT PRAL OFFICE IN ISLAMABAD

1.	Pakistan Revenue Automation (Pvt.) Ltd. (hereinafter called PRAL/Purchaser) invites sealed bids for supply & installation of 60 KVA Generator and 30 KVA UPS (one each) at PRAL office, House # 2-A, Embassy Road, Sector G-6/4, Islamabad. Detail specifications of the Generators and UPS are given in the Schedule of Requirement attached at Annexure “A”.

2.	If you have any doubt as to the meaning of any portion of the technical specifications, you may seek clarification of the same from Malik Nasir Abbas, Manager (Infrastructure) PRAL Cell # 0321-5371151.

3.	PRAL reserves the right to increase or decrease the above quantity, accept or reject any bid to be received against this tender inquiry, annul the bidding process and reject all bids at any time prior to award of Contract (s) without thereby incurring any liability to the affected Bidder or Bidders or any obligation to inform the affected Bidder or of the grounds for PRAL’s action.

4.	Income Tax / Withholding Tax will be deducted in accordance with the law. Kindly note that the Sales Tax shall also be deducted in accordance with the law.

5.	DELIVERY SCHEDULE

The delivery / installation of the equipment mentioned in the attached Annexure “A” is required on URGENT BASIS at house # 2-A, embassy road, G-6/4, Islamabad. So the lowest technical compliant bidder may be in a position to deliver/install the equipment immediately after award of the contract(s), therefore the bidders are required to quote shortest possible delivery & installation time.

6.	PENALTY:

For failure to comply with the delivery schedule of Purchase Order (s), to be issued against this tender documents penalty will be imposed on defaulting Supplier as under:

6.1	1% of the cost of entire purchase order or of such item as remains un-supplied/un-completed for every day up to maximum of 5% for 10 days exceeding the delivery period.

6.2	If the item is not supplied even after payment of penalty for 10 consecutive days PRAL reserves the right to cancel the purchase order and to purchase required equipment from elsewhere at risk and cost of the defaulting Supplier.

7.	Quoted prices must be inclusive of all taxes (Income Tax and Sales Tax), indicating unit price and total bid price.

8.	Price must be quoted including all charges like handling, loading, transportation, unloading of the equipment at above location. Quoted prices must also be inclusive of cost for the free maintenance of equipment on installation site during warranty period.

9.	Bidding Form must also be duly filled in, stamped and signed by authorized representative of the bidder.

10.	Quoted price shall be valid for 90 days from the opening date of the bids. However, any subsequent change in taxes and duties as notified by Federal Board of Revenue will be given due consideration.

11.	EARNEST MONEY:

The Bidder shall furnish as part of his bid, a Call Deposit/Pay Order equivalent to 2% of the total bid value as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.”. Bank Guarantee as earnest money will not be entertained. Any bid not accompanied by Earnest Money shall be rejected without any right of appeal. In case of cancellation of Purchase Order as default of the Supplier the earnest money shall be forfeited in favour of PRAL.

12.	PAYMENT:

100% payment of the total value of the bill/purchase order will be released subject to:

12.1.	Completion of the delivery/installation of the equipment in accordance with the specifications mentioned in this tender document or Purchase Order(s) to be issued against this tender;

12.2.	Submission of Bank Guarantee (to be issued by any renowned schedule bank), being 10% of the total bill value for the warranty period. The Bank Guarantee shall be released after successful completion of warranty period. Failing to provide bank guarantee 10% of the bill shall be retained till to the successful expiry of the warranty period;

13.	SEALING AND MARKING OF BIDS.

13.1	The bids shall be submitted in sealed envelope marked as under:

Manager (Procurement)

House # 2-A, Main Embassy Road, Sector G-6/4, Islamabad.

13.2	The envelopes shall also bear the word “CONFIDENTIAL” and following identifications:-

BID NO. ADMIN (G-08)/2012

For supply & installation of 60 KVA Generator and 30 KVA UPS.

14.	DEADLINE FOR SUBMISSION OF BIDS:

All bids must be delivered in the Office of undersigned on or before the prescribed deadline of 1100 hours on 10/10/2012.

15.	OPENING OF BIDS:

The Purchaser will open the bids in the presence of bidder representatives who choose to attend at 1130 hours on 10/10/2012 at the below mentioned address.

16.	WARRANTY

16.1	The Supplier shall warrant that all equipment supplied against the Purchase Order (s) shall have no defect arising from design, materials or workmanship or from any act or omission of the Supplier that may develop under normal use of the supplied items under the conditions prevailing at final destination.

16.2	Period of Warranty and maintenance with labour and material cost shall be minimum one (01) year comprehensive” (including batteries).

During warranty period the supplier will be responsible to repair/replace the faulty equipment on installation place free of cost within 24 hours after occurrence of fault. During warranty period due to any reason, if the Supplier failed to rectify the problem, PRAL shall repair the equipment or replace the defective parts thereof and forfeit the Bank Guarantee/retained values.

17.	All bids should include:

17.1	Company’s profile, list of clients with their telephone number and address;

17.2	Copies of Income Tax and Sales Tax registration certificates;

17.3	A call deposit being, 2% of the total bid value, as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.; and

17.4	Brochures and other technical material of the quoted equipment.

18.	PRAL reserves the right to increase or decrease the quantity of the equipment / or scope of work or may cancel any or all tender work shown in Annexure “A”.

# (SOHAIL AKHTAR)

Manager (Procurement)

House # 2-A, Main Embassy Road, Sector G-6/4, Islamabad.

Phone: 9208687

ANNEXURE-A

BILL OF QUANTITY (BOQ):

TENDER # ADMIN (G-08)/2012, DATED 25/09/2012

Bill of Quantity

| S. No | DESCRIPTION | Quantity |
| --- | --- | --- |
|  | 60 KVA Diesel Generator with turnkey installation and commissioning | 1 |
|  | 30 KVA UPS with all jobs along with turnkey installation and commissioning | 1 |

## TECHNICAL SPECIFICATIONS

## 60 KVA Generator

Only Branded  Generators like Perkisn, Cummins, SDMO etc or equivalent (100% Imported brand) with foregin coupled Alternator is acceptable with imported orignal manufacturers installed control panel generators are acceptable. No local assembled brands of any even foregin brands is acceptable.

- 3 Phase (69 Ampere per Phase Out put)

- Rated Frequency (Hz) 50-60 Hz

- Rate Voltage (AC) (V) 400 / 230

- Rated Current (AC) (A) 69

- Power Factor (COSΦ)  0.8 (lag)

- Power Supply AC, 3-phase, 4-lines

- Type In-line, 4-strokes, water cooled, direct injection, diesel engine

- Number Of Cylinders: 4 in line.

Auto Transfer Switch Panel

- ATS  designed for 60 KVA Generators with all safety features and (branded Schneider electric/ABB Contactors with all best components is acceptable)

Acoustic weather proof Canopy

- Fresh air provided through Acoustic Louvers.

- Hinged and lockable door all around Canopy for easy access to DG Set for routine maintenance.

Cable

- 35 mm 4 core PVC/PVC with GI Conduit should be ISO certified with applicable BS standards.

RCC Foundation Pad & Earth Pits

- RCC foundation and unit Earthing with (with 25mm PVC coated branded grounding wire (2 earth pits minimum) and commissioning.

Turnkey installation of the generator

- Complete turkey installation/ commissioning of the 60 KVA generator complete in all respect which includes all above components and necessary jobs for commissioning.

## 30 KVA UPS

- 30-KVA true on-line with extended battery bank with 30 Minutes backup on full load

- Complete digital LCD control & display

- On-Line Double Conversion

- Pure sine wave with efficiency more than 97%.

- Apparent Power 30-KVA

- Active Power  24-KW

- Capable of parallel attachment (N+1) of up-to 4 units or more in case of increase in load. (Parallel add in facility of new UPS in the existing environment).

- Hot stand-by redundant & parallel function.

- Input range: 220, 440VAC single / three input phase. Output 220 VAC single / three input phase

- Galvanic isolation.

- Scheduling facility for battery testing & UPS controls.

- Intelligent power interface with management software

- Capable of remote monitoring & Management

- Fully compatible with all generators.

- EPO capable (Emergency Power Off)

- Built-In protection against surges, spikes, over & under voltage and

- short circuit.

- Built-in stabilizer.

- Cold start facility.

- Battery overcharging protection.

- 3-Phase Input & 3-Phase Output

- Sealed Dry Batteries VRLA (value regulated lead acid)

Power Distribution Board for (Input and output)

- 30KVA ups distribution Separate Input/output DBs complete with digital meter for volt and AMP and 12 units for 20 AMP SP – 12 units for  16 AMP SP – five  32 AMP SP and main TP 100 AMP.

Turnkey installation of the UPS

- Complete turkey installation/ commissioning of the UPS complete in all respect which includes 16mm2 four core PVC/PVC 99.99% (Pakistan cable) for input and output circuits and necessary jobs for commissioning. (survey is recommended for exact calculation and solution understanding)

BIDDING FORM

##### Dated 25/09/2012

##### Tender No.ADMIN (G-08)/2012

Pakistan Revenue Automation (Pvt.) Limited, Islamabad.

Gentlemen,

1.	Having examined the conditions to Tender and Specifications of Tender No.ADMIN (G-08)/2012 dated September 25, 2012 the receipt of which is hereby acknowledged we, the undersigned, offer to install, supply and deliver in conformity with specifications mentioned in Annexure “A” and conditions of Tender for the sum of Rs._________________________ (Rupees ______________________________ ) or such other sums as may be ascertained in accordance with the said Conditions.

2.	If our Bid is accepted we shall deliver / commenced the equipment / services mentioned in the tender documents within ______ days from the date of receipt of your firm Purchase Order / Work Order.

3.	We agree to abide by the terms and conditions of the Tender for the period of _______ from the date fixed for receiving the same and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

4.	Until a formal Purchase order(s) is placed, this Bid, together with your written acceptance thereof, shall constitute a binding contract between us.

5.	We understand that you are not bound to accept the lowest or any proposal you may receive or to inform us of the rejection of our bid or to give any reasons therefore.

Dated this ______________________ day of ______________________________ 2012_______________.

Signature _______________________ in the capacity of ______________________________ duly authorized to sign Tender for and on behalf of

_____________________________________________________________________________________

(NAME OF FIRM IN BLOCK CAPITALS)

Complete address:________________________________________________________________________

Fax No.____________________________ Telephone No.______________________________________

______________________

( SIGNATURE )

Witness:-

1.	_______________________

2.	_______________________