PAKISTAN REVENUE AUTOMATION (PVT.) LIMITED

Tender No. P-20/2013

Dated 14/06/2013

BIDS SUBMISSION: 29/06/2013 ON OR BEFORE 1500 HOURS

BIDS OPENING DATE AND TIME: 29/06/2013 AT 1530 HOURS

Subject:	TENDER NO. P-20/2013 DATED 14/06/2013 FOR SUPPLY & INSTALLATION OF NETWORKING EQUIPMENT / ITEMS

1.	Pakistan Revenue Automation (Pvt.) Ltd. (hereinafter called PRAL/Purchaser) invites sealed bids for the supply & installation of networking equipment /items at Sector I-9/3, Islamabad as per detail / specifications described in the BOQ “Annexure- A”.

2.	All Government Taxes shall be deducted as per law.

3.	PRAL reserves the right to increase or decrease the quantity mentioned in the Schedule of Requirement Annexure “A”, accept or reject any bid to be received against this tender inquiry, annul the bidding process and reject all bids at any time prior to award of Contract (s). Justification of the rejection of bid (s) will be provided on request.

4.	DELIVERY SCHEDULE

The Supply & Installation of networking equipment / items is required on most urgent basis. So the lowest technical compliant bidder may be in a position to supply and install the order material as immediately as possible after award of the contract.

5.	PENALTY:

For failure to comply with the delivery schedule of Purchase Order (s), to be issued against this tender documents penalty will be imposed on defaulting Supplier as under:

5.1	1% of the cost of entire purchase order or of such item as remains un-supplied/un-completed for every day up to maximum of 5% for 10 days exceeding the delivery period.

5.2	If the item is not supplied even after payment of penalty for 10 consecutive days PRAL reserves the right to cancel the purchase order and to purchase required equipment from elsewhere at risk and cost of the defaulting Supplier.

6.	Quoted prices must be inclusive of all taxes (Income Tax and Sales Tax), indicating unit price and total bid price.

7.	Price must be quoted including all charges like handling, loading, transportation, unloading of the material.

8.	Bidding Form Annexure “B” must also be duly filled in, stamped and signed by authorized representative of the bidder.

9.	Quoted price shall be valid for 120 days from the opening date of the bids. However, any subsequent change in taxes and duties as notified by Federal Board of Revenue will be given due consideration.

10.	PAYMENT:

100% payment of the total value of the bill/purchase order will be released subject to Completion of the delivery of the equipment / jobs in accordance with the specifications mentioned in this tender document or Work Order to be issued against this tender and submission of bank guarantee as described under clause “16” of the tender documents.

11.	SEALING AND MARKING OF BIDS.

11.1	The bids shall be submitted in sealed envelope marked as under:

MANAGER (PROCUREMENT)

PAKISTAN REVENUE AUTOMATION (Pvt.) LIMITED

HOUSE # 2-A, EMBASSAY ROAD, G-6/4, ISLAMABAD

11.2	The envelopes shall also bear the word “CONFIDENTIAL” and following identifications:-

BID NO. P-20/2013

For the supply & installation of Networking Equipment / Items

12.	DEADLINE FOR SUBMISSION OF BIDS:

All bids must be delivered in the Office of undersigned on or before the prescribed deadline of 1500 hours on 29/06/2013.

13.	OPENING OF BIDS:

The Purchaser will open the bids in the presence of bidder representatives who choose to attend at 1530 hours on 29/06/2013 at the below mentioned address.

14.	WARRANTY

14.1	The Supplier shall warrant that all equipment supplied against the Purchase Order (s) shall have no defect arising from design, materials or workmanship or from any act or omission of the Supplier, that may develop under normal use of the supplied items under the conditions prevailing at final destination.

14.2	Period of Warranty and maintenance with labour and material cost shall be SIX (06) Months except Networks Switches. The Network Switches shall be under one (01) year warranty.

During warranty period the supplier will be responsible to repair/replace the faulty item (s) on installation place free of cost within 24 hours after occurrence of fault

15.	If you have any doubt as to the meaning of any portion of the technical specifications, you may seek clarification of the same from Mr. Muhammad Usman, Director PRAL, House # 14, Hill Road, Sector F-6/3, Islamabad Cell # 0321-5576257.

16.	BANK GUARANTEE

After completion and acceptance of the Project by PRAL, the bidder will have to provide the Bank Guarantee, being 10% of the total value of the bill/Contract, issued by renowned Schedule Bank, for the warranty/maintenance period to be offered. In case the supplier failed to provide the Bank Guarantee 10% of the total bill value shall be retained by PRAL for the successful completion of warranty period. The Bank Guarantee shall be released after successful completion of warranty period. In case the supplier failed to complete the warranty period successfully then the retained value/bank guarantee shall be forfeited in favour of PRAL.

17.	EARNEST MONEY:

The Bidder shall furnish as part of his bid, a Call Deposit/Pay Order equivalent to 2% of the cost as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.”. Any bid not accompanied by Earnest Money shall be rejected without any right of appeal. In case of cancellation of the contract as default of the successful bidder (s) the earnest money shall be forfeited in favour of PRAL.

18.	All bids should include:

18.1	Company/firm name with complete address with detail landline number, fax, etc

18.2	Company’s profile, list of clients with their telephone number and address;

18.3	Copies of Income Tax and Sales Tax registration certificates; and

18.4	Earnest money as per clause 18 of the tender documents.

.

(SOHAIL AKHTAR)

Manager (Procurement)

HOUSE # 2-A, EMBASSAY ROAD, G-6/4, ISLAMABAD

Phone:	051-9208687

ANNEXURE-A

SCHEDULE OF REQUIREMENT

TENDER # P-20/2013 DATED 14/06/2013

SUPPLY, INSTALLATION OF NETWORKING EQUIPMENT/ITEMS

| S.# | Description | Quantity | Unit | Unit Rate |
| --- | --- | --- | --- | --- |
| 1. | Layer 3 Switch 24 port (specs attached) | 1 | Unit |  |
| 2. | Layer 2 Switches 24 port Gigabits (specs attached) | 15 | Unit |  |
| 3. | Complete I/O, Faceplate, Box of 3M/Systemax/Panduit/Clipsal brand with installation | 250 | Unit |  |
| 4. | Patch Panel for Consolidation 24 port with I/O of 3M/Systemax/Panduit/Clipsal brand | 4 | Unit |  |
| 5. | Cat6 Cable Rolls | 15 | Rolls |  |
| 6. | Complete laying of CAT 6 Cable, including crimping, tagging, etc | 250 | Nodes |  |

| Layer 3 Switch Specifications |
| --- |
| Forwarding performance: | 96 Mpps |
|  | Double hot swappable power supplies |
|  | 24 x 10/100/1000Base-T ports |
|  | 4x1000Base-X SFP ( with modules for Ethernet) |
| MAC address table | IEEE 802.1d compliance |
|  | 32K MAC |
|  | MAC address learning and aging |
|  | Static, dynamic, and blackhole MAC address entries |
|  | Packet filtering based on source MAC addresses |
| VLAN | 4 K VLANs |
|  | Guest VLAN and voice VLAN |
|  | VLAN assignment based on MAC addresses, protocols, IP subnets, policies, and ports |
|  | 1:1 and N:1 VLAN Mapping |
| Reliability | RRPP ring topology and RRPP multi-instance |
|  | Smart Link tree topology and Smart Link multi-instance, providing the millisecond-level protection |
|  | switchover |
|  | SEP |
|  | BFD for OSPF, BFD for IS-IS, BFD for VRRP, and BFD for PIM |
|  | STP, RSTP, and MSTP |
|  | BPDU protection, root protection, and loop protection |
|  | E-Trunk |
| IP routing | Static routing, OSPF, OSPF v3, IS-IS, IS-ISv6, BGP, BGP 4+, and ECMP |
| IPv6 features | Neighbor Discovery (ND) |
|  | Path MTU (PMTU) |
|  | IPv6 ping, IPv6 tracert, and IPv6 Telnet |
|  | ACLs based on the source IPv6 address, destination IPv6 address, Layer 4 ports, or protocol type |
|  | MLD v1/v2 snooping |
|  | 6to4 tunnel, ISATAP tunnel, and manually configured tunnel |
| multicast | IGMP v1/v2/v3 snooping and IGMP fast leave |
|  | Multicast forwarding in a VLAN and multicast replication between VLANs |
|  | Multicast load balancing among member ports of a trunk |
|  | Controllable multicast |
|  | Port-based multicast traffic statistics |
|  | IGMP v1/v2/v3, PIM-SM, PIM-DM, and PIM-SSM |
|  | MSDP |
| QoS/ACL | Rate limiting on packets sent and received by an interface |
|  | Packet redirection |
|  | Eight queues on each port |
|  | WRR, DRR, SP, WRR+SP, and DRR+SP queue scheduling algorithms |
|  | WRED |
|  | Re-marking of the 802.1p priority and DSCP priority |
|  | Packet filtering at Layer 2 to Layer 4, filtering out invalid frames based on the source MAC address, |
|  | destination MAC address, source IP address, destination IP address, port number, protocol type, |
|  | and VLAN ID |
|  | Rate limiting in each queue and traffic shaping on ports |
| Security | User privilege management and password protection |
|  | DoS attack defense, ARP attack defense, and ICMP attack defense |
|  | Binding of the IP address, MAC address, interface, and VLAN |
|  | Port isolation, port security, and sticky MAC |
|  | Blackhole MAC address entries |
|  | Limit on the number of learned MAC addresses |
|  | 802.1x authentication and limit on the number of users on an interface |
|  | AAA authentication, RADIUS authentication, HWTACACS+ authentication, and NAC |
|  | SSH v2.0 |
|  | Hypertext Transfer Protocol Secure (HTTPS) |
|  | CPU defense |
|  | Blacklist and whitelist |
| Management and maintenance | Stacking |
|  | MAC Forced Forwarding (MFF) |
|  | Virtual cable test |
|  | Port mirroring and RSPAN (remote port mirroring) |
|  | Remote configuration and maintenance by using Telnet |
|  | SNMP v1/v2/v3 |
|  | RMON |
|  | Web NMS |
|  | System logs and alarms of different levels |
| Operating environment | Operating temperature: 0 to 50 degree |
|  | Relative humidity: 10%–90% (non-condensing) |
| Input voltage | AC:220 |

| Layer 2 Switch Specifications |
| --- |
| Downlink port | 24 x 10/100/1000 M |
| Uplink port | 2 GE SFP optical ports (with Modules for Ethernet) |
| MAC address table | 8 K MAC |
|  | Packet filtering based on MAC addresses |
|  | MAC address authentication |
|  | Port-based 802.1x authentication. |
|  | RADIUS authentication |
|  | Port isolation |
|  | Storm suppression |
|  | Attack defense, which prevents broadcast traffic, ARP attacks, ICMP attacks, TCP attacks, worm viruses, and DoS attacks |
|  | DHCP snooping |
| VLAN | 4 K VLANs |
|  | Access port |
|  | Trunk port |
|  | Hybrid port |
|  | Management VLAN |
|  | Voice VLAN |
| QOS | PQ and WRR |
|  | Four queues on each port |
|  | Queue scheduling based on 802.1p or DSCP priorities |
| STP | STP/RSTP/MSTP |
| Multicast | IGMP snooping and a maximum of 256 multicast groups |
| Link aggregation | 12 link aggregation groups (LAGs) and a maximum of eight ports in each LAG |
|  | Static LACP |
| Port mirroring | Port-based bidirectional flow mirroring |
|  | Configuring a trunk as a mirrored interface |
| Bandwidth control | Rate limiting for incoming and outgoing packets, with the granularity of 64 kbps |
| Broadcast storm suppression | Broadcast storm suppression based on the interface rate |
|  | Sending alarms when the traffic rate reaches the upper limit |
| Device management | SNMP |
|  | Web system network management (HTTPS) |
|  | DHCP client |
|  | User password protection |
|  | One-key restoration |
| Device maintenance | Remote Network Monitoring (RMON) |
|  | System log |
|  | Ping and traceroute |
|  | Virtual Cable Test (VCT) |
|  | Link Layer Discovery Protocol (LLDP) |
| Packet forwarding rate | 9.6 Mbps |
| Switching capacity: | 12.8 Gbps |

Note: 	For any query regarding technical specifications of the equipment please contact Mr. Muhammad Usman, Director PRAL, House # 14, Hill Road, Sector F-6/3, Islamabad Cell # 0321-5576257.

ANNEXURE-"B"

BIDDING FORM

Dated 14/06/2013

Tender No.P-20/2013

Pakistan Revenue Automation (Pvt.) Limited, Islamabad.

Gentlemen,

1.	Having examined the conditions to Tender and Specifications of Tender No.P-20/2013 dated 14/06/2013 the receipt of which is hereby acknowledged we, the undersigned, offer to install, supply and deliver in conformity with specifications mentioned in Annexure “A” and conditions of Tender for the sum of Rs._________________________ (Rupees ______________________________ ) or such other sums as may be ascertained in accordance with the said Conditions.

2.	If our Bid is accepted we shall deliver the equipment mentioned in the tender documents within ______ days from the date of receipt of your firm Purchase Order.

3.	We agree to abide by the terms and conditions of the Tender for the period of _______ from the date fixed for receiving the same and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

4.	Until a formal Purchase order(s) is placed, this Bid, together with your written acceptance thereof, shall constitute a binding contract between us.

5.	We understand that you are not bound to accept the lowest or any proposal you may receive or to inform us of the rejection of our bid or to give any reasons therefore.

Dated this ______________________ day of ______________________________ 2013_______________.

Signature _______________________ in the capacity of ______________________________ duly authorized to sign Tender for and on behalf of

_____________________________________________________________________________________

(NAME OF FIRM IN BLOCK CAPITALS)

Complete address:________________________________________________________________________

Fax No.____________________________ Telephone No.______________________________________

______________________

( SIGNATURE )

Witness:-

1.	_______________________

2.	_______________________