CORRIGENDUM

TENDER NOTICE NO. P-05/2019 DATED 13/02/2019

Reference our Tender Notice No. P-05/2019 dated 13/02/2019 uploaded on PPRA‘s and PRAL’s websites for the purchase of dry batteries for UPS. The existing Annexure-A of the tender documents has been replaced with the Annexure-A as below:

ANNEXURE-A

SCHEDULE OF REQUIREMENT

TENDER # P-05/2019 DATED 13/02/2019

SPECIFICATION FOR SUPPLY OF DRY BATTERIES REQUIRED FOR UPS

| S. # | Description | Qty. | Delivery |
| --- | --- | --- | --- |
| 1. | CSB 12V, 9AH Sealed Dry charged UPS Batteries 5 years design life with 1 Year warranty for APC Symmetra PX160KVA UPS Battery Modules Panasonic or equivalent internationally recognized brands only. Model No. UP-PW1245P1 (Existing Batteries detail) Type Brand: Panasonic (Value Regulated Lead-Acid Battery) Rated Voltage Rating 12VDC Capacity: 9.0 Ah Weight: 2.60 kg Standby Use: 13.6V-13.8V (25C) Rated Capacity: 270W (10 minutes power discharge, equivalent to approximately 8Ah discharge capacity of 20 h) Terminal types: F2 terminal – Faston Tab 250 Container Material: ABS (UL 97-HB) & Flame Retardant (94-V0) Dimensions: Length (L): 150.9±2.0 mm 5.9±0.08 inch Width (W): 64.8±1.0 mm 2.55±0.04 inch Container Height (H): 94.3±1.0 mm 3.71±0.04 inch Overall Hight (H): 98.6±1.0 mm 3.88±0.04 inch | 144 | Datacenter, FBR House, Islamabad |
| 2. | 12V – 17Ah Sealed Dry charged UPS Batteries FOR 60KVA Eaton UPS with 5 years design life with 1 Year warranty. | 40 | 9th Floor, Custom House, Karachi |

The last date for submission and opening of bids is also extended from 28/02/2019 to 01/03/2019 on or before 1500 hours. The bids will be opened on 01/03/2019 at 1530 hours. All others terms and conditions mentioned in the tender document will remain the same.

Manager (Procurement & Inventory)

2nd Floor, Software Technology Park, Plot No.156, Service Road North, I-9/3, Islamabad.

Ph: 051-9259353/9259354