TENDER DOCUMENTS

PAKISTAN REVENUE AUTOMATION (PVT) LIMITED

TENDER No. P-12/2019

DATED 22/05/2019

BIDS SUBMISSION: 11/06/2019 ON OR BEFORE 1100 HOURS

BIDS OPENING DATE AND TIME: 11/06/2019 AT 1130 HOURS

### Subject:	PURCHASE OF APC IT POWER DISTRIBUTION MODULES 3X1 POLE 3 WIRE 32A 3XIEC309, AND FLEXIBLE POWER CABLE 3-CORE 10MM2 FOR SYMMETRA PX APC 160KVA UPS.

Pakistan Revenue Automation (Pvt.) Ltd. (hereinafter called PRAL/Purchaser) invites sealed bids from the firms registered with the Sales Tax & Income Tax department and who are also on active tax payer list of FBR for the supply of APC IT Power Distribution Modules 3x1 Pole 3 Wire 32A 3xIEC309, and Flexible Power Cable 3-Core 10mm2 for Symmetra PX APC 160KVA UPS as per specifications mentioned in Annexure “A”.

1.	If you have any doubt as to the meaning of any portion of the technical specifications, you may seek clarification of the same from Syed Muhammad Aamir, Network Administrator (PRAL). Ph:051-9259358 Cell # 0333-1944326.

2.	Income Tax / Withholding Tax will be deducted in accordance with the law. Kindly note that the Sales Tax (if applicable) shall also be deducted in accordance with the law.

3.	PRAL reserves the right to increase or decrease the quantity of the required items(As per Annexure-A) , accept or reject any bid to be received against this tender inquiry, annul the bidding process and reject all bids at any time prior to award of Contract (s). Justification of the rejection of bid (s) will be provided on request.

4.	DELIVERY SCHEDULE

The delivery (at Islamabad) of the Items (as per Annexure-A) is required ON URGENT BASIS so the bidders are required to quote shortest possible delivery time. Delivery period of the quoted Items must be mentioned clearly.

5.	Quoted prices must be inclusive of all applicable taxes and delivery (at Islamabad) charges of the Items.

6.	Price must be quoted including all charges like handling, loading, and transportation etc. Quoted prices must also be inclusive of cost for the free maintenance of the Power Distribution Modules (PDM) on installation site (during warranty period).

7.	Quoted price shall be valid for ninety (90) days from the opening date of the bids. However, any subsequent change in taxes and duties as notified by Federal Board of Revenue will be given due consideration.

08.	PAYMENT:

Payment will be made as per mutually agreed schedule and in accordance with the terms and conditions spelled out in the contract issued against this tender document. However, submission of Bank Guarantee, being 10% of the total bill value/ Work Order / Purchase Order Value shall be pre-requisite for the release of 100% payment. The Bank Guarantee must be issued by Schedule Bank. The Bank Guarantee shall be released after successful completion of warranty period. In case the supplier failed to complete the warranty period successfully then the retained value/bank guarantee shall be forfeited in favor of PRAL. For any advance payment the Bank Guarantee shall be required.

09.	SEALING AND MARKING OF BIDS:

9.1	The bids shall be submitted in sealed envelope marked as under:

MANAGER (P&I)

PAKISTAN REVENUE AUTOMATION (Pvt.) LIMITED

2nd Floor, Software Technology Park (STP), Sector, I-9/3, Islamabad.

9.2	The envelopes shall also bear the word “CONFIDENTIAL” and following identifications: -

BID NO. P-12/2019 Dated 22/05/2019

SUPPLY OF APC IT Power Distribution Modules 3x1 Pole 3 Wire 32A 3xIEC309, 300CM, 360Cm and Flexible Power Cable 3-Core 10mm.

10.	DEADLINE FOR SUBMISSION OF BIDS:

All bids must be delivered in the Office of undersigned on or before the prescribed deadline of 1100 hours on 11/06/2019.

11.	LATE PROPOSALS:

Any bid received by PRAL after the prescribed deadline will be returned unopened to the Bidder.

12.	OPENING OF BIDS:

The Purchaser will open the bids in the presence of bidder representatives who choose to attend at 1130 hours on 11/06/2019 at the above-mentioned address under clause 9.1.

13.	EVALUATION:

13.1.	After opening, PRAL will examine the bids for financial and technical evaluation and completeness of the same as per tender requirements.

13.2.	Bidder (s) who does not qualify cannot challenge the findings of the evaluation or ask for reasons of disqualification.

14.	WARRANTY

14.1	The Supplier shall warrant that the equipment supplied under the Contract (s) shall have no defect arising from design, materials or workmanship or from any act or omission of the Supplier, which may develop under normal use of the supplied items under the conditions prevailing at final destination.

14.2	PRAL shall promptly notify the Supplier in writing of any claims arising under this Warranty. Upon receipt of such notice, the Supplier shall repair or replace the defective equipment or parts thereof, without cost to PRAL immediately.

14.3	Period of comprehensive warranties and maintenance with labor and material cost shall be minimum one (01) year.

During the warranty period due to any reason, if the Supplier failed to rectify the problem, PRAL shall get repair the equipment or replace the defective parts thereof and forfeit the Bank Guarantee/retained values.

15.	EARNEST MONEY:

The Bidder shall furnish as part of his bid, a Call Deposit/Pay Order equivalent to 2% of the total bid value as Earnest Money crossed in favour of “Pakistan Revenue Automation (Pvt.) Ltd.”. Any bid not accompanied by Earnest Money shall be rejected without any right of appeal. In case of cancellation of Purchase Order as default of the Supplier the earnest money shall be forfeited in favor of PRAL.

16.	PENALTY:

For failure to comply with the delivery schedule of Purchase Order (s), to be issued against this tender inquiry, penalty will be imposed on defaulting Supplier as under:

16.1	1% of the cost of entire purchase order or of such item as remains un-supplied/un-completed for every day up to maximum of 5% for 10 days exceeding the delivery period.

16.2	If the item is not supplied even after payment of penalty for 10 consecutive days PRAL reserves the right to cancel the purchase order and to purchase required equipment from elsewhere at risk and cost of the defaulting Supplier.

17.	The bidders will be required to provide following:

17.1	Company’s profile,

17.2	Evidence for Income Tax and Sales Tax Registration;

18.	Bidding Form Annexure “B” must also be duly filled in, stamped and signed by authorized representative of the bidder.

(NADEEM ANWAR)

Manager (Procurement & Inventory)

2nd floor, Software Technology Park (STP), I-9/3, Islamabad.

Ph: 051-9259353, Cell 0306-5511272

Email: nadeem.anwar@pral.com.pk

ANNEXURE-A

SCHEDULE OF REQUIREMENT

TENDER # P-12/2019 DATED 22/05/2019

SPECIFICATION FOR SUPPLY OF APC IT POWER DISTRIBUTION MODULES 3X1 POLE 3 WIRE 32A 3XIEC309, 300CM, 360CM AND FLEXIBLE POWER CABLE 3-CORE 10MM.

| S. # | Description | Qty. | Delivery |
| --- | --- | --- | --- |
| 1 | APC IT Power Distribution Modules 3x1 Pole 3 Wire 32A 3xIEC309, 300cm, 360cm. Model No. PDM1332IEC-3P PDM1332IEC-3P Features Factory assembled and tested Power Distribution Modules include circuit breaker, power cord, power connection, and circuit monitoring. Auto-detection of modules by the Modular PDU minimizes installation time. Multiple distribution options: Superior design flexibility enables a wide range of customer requirements to be addressed. System mobility: Power distribution units can easily be relocated to accommodate a changing data centre environment. Modular Power Accessories Features & Benefits Manageability Power monitoring: Measure and monitor power consumption and usage with branch circuit monitoring and output metering, which are included at no extra cost Quick status information LEDs: Access status information about the performance of the Power Distribution Module Safety Safety, enhance user safety with isolation at all touch points and with positive locking mechanisms that reduce the risk of accidental disconnection Convenience Toolless installation of breakers: Install factory-assembled Power Distribution Modules in under ten minutes - no tools are required Global product offering: Standardization of power distribution units across all corporate locations is easy-a variety of 1-phase and 3-phase Power Distribution Modules address the unique power requirements of data centers around the world. Technical Specifications Model No. PDM1332IEC-3P Output Nominal Output Voltage 230V Maximum Total Current Draw 32 Input Nominal Input Voltage 400V 3PH Input frequency 50 Hz Maximum Line Current 32A Physical Maximum Height 152mm, 15.2CM Maximum Width 432mm, 43.2CM Maximum Depth 152mm, 15.2CM Net Weight 6.39KG Shipping weight 7.3KG Shipping Height 152mm, 15.2CM Shipping Width 432mm, 43.2CM Shipping Depth 152mm, 15.2CM Conformance Approvals CE, VDE Standard warranty 5-year repair or replace | 04 | Datacenter FBR House, Islamabad |
| 3 | Flexible Power Cable 3-Core 10mm2 Technical Specifications: Brand Name: Pakistan Cable Product name: 3-Core 10mm2 Flexible Power Cable Type: Insulated Rated Voltage: 230 to 1000V AC Conductor Type: Strand Conductor Material: Tinned copper Color: Yellow, Red, Black Rated Temperature: -60°C~200°C Gauge: AWG 10mm2 Full Gauge | 135 Meter | Datacenter FBR House, Islamabad |

GENERAL TERMS & CONDITIONS

- The prices should be valid for 90 days.

- No advance payments will be made.

- 2% earnest money of the total bid value. In case more options are quoted, vendor will submit earnest money for each option separately.

- The award of contract will purely be done on the technical compliance and subsequent evaluation.

- Government duties and taxes should be separately mentioned in the Financial Proposal, if applicable.

- The warranty period will start after the issuance of Job Completion Certificate.

- The decision for the award of Contract cannot be challenged anywhere

- The firms black-listed/ debarred in participating in any procurement activities in Pakistan are not allowed to bid.

- Submission of compliance sheet is a must.

ANNEXURE-"B"

BIDDING FORM

TENDER # P-12/2019 DATED 22/05/2019

Pakistan Revenue Automation (Pvt.) Limited, Islamabad.

Gentlemen,

1.	Having examined the conditions to Tender and Specifications of Tender No. P-12/2019 dated 22/05/2019 the receipt of which is hereby acknowledged we, the undersigned, offer to install, supply and deliver in conformity with specifications mentioned in tender documents and conditions of Tender for the sum of Rs._________________________ (Rupees ________________________________________________________________ ) or such other sums as may be ascertained in accordance with the said Conditions.

2.	If our Bid is accepted, we shall deliver the equipment mentioned in the tender documents within ______ days from the date of receipt of your firm Purchase Order.

3.	We agree to abide by the terms and conditions of the Tender for the period of _______ from the date fixed for receiving the same and it shall remain binding upon us and may be accepted at any time before the expiration of that period.

4.	Until a formal Purchase order(s) is placed, this Bid, together with your written acceptance thereof, shall constitute a binding contract between us.

5.	We understand that you are not bound to accept the lowest or any proposal you may receive or to inform us of the rejection of our bid or to give any reasons therefor.

Dated this ____________________ day of ______________________________________ 2019.

Signature _________________ in the capacity of __________ duly authorized to sign Tender for and on behalf of

______________________________________________________________________________ (NAME OF FIRM IN BLOCK CAPITALS)

Complete address: _______________________________________________________________

Fax No.____________________ Telephone & Cell No.__________________________________

______________________

(SIGNATURE)

Witness: -

1.	_______________________ 2.	_________________________